Error Propagation

- Determining Absolute  Uncertainty

___ For direct read scales- ± ½ of the smallest unit

___ For digital read instruments- ± 1 of the least place value reported

___ For probeware- manufacturer’s reported value

- Absolute Uncertainty - Addition and Subtraction.

___ Add absolute uncertainties of manipulated values.

∆T = 100.0oC – 38.7oC    = 61.3oC±0.10oC

±0.05oC  - ±0.05oC  = ±0.10oC

- Determining % Uncertainty

___ For a single entry-     abs. uncert.	x 100 =

measured value

61.3oC ±0.10oC     =  ±0.10oC/61.3 x 100= 0.016% (round sig figs)= 0.02%

61.3oC±0.02%

___ For manipulated values- convert each value entered to % uncertainty, then add all

% uncertainties together.

Find % uncertainty:

Mass       0.01g/50.00g x100= 0.02%

Cp  	     0.01/4.18 x 100 = 0.2%

∆T	     0.10oC/61.3 x 100= 0.02%

Heat = mass(∆T)Cp  		to find heat

Heat = 50.00g(61.3oC)4.18J/goC = 12811.7J±0.2% (round sig figs)= 12800jJ±0.2j%

0.02% + 0.02% + 0.2% = 0.24 ≈ ±0.2%

To convert back to absolute uncertainty:

12800J x 0.002 = ±25.6J      therefore	12800J±25.6J